## Slide 1
state: ACTIVE
state: Init
The system is performing a checklist of tests to confirm the operational integrity of the sub-system components. Some of these tests are bypassed when resuming from a paused state.
state: Goto_Payload_Bay
state: Scan
Camera feed is processed at a stable sampling rate to identify the payload bay compartment.
state: Plan/Look-ahead/Move
Using the relative position and orientation of the bay, the arm plans a move towards the bay, instructing the motors with relevant signals.
state: Retrieve_Sample
state: Scan
Camera feed is processed to identify the sample on the ground
state: Plan/Look-ahead/Move
Using the relative position and orientation of the sample, the arm plans a move towards the sample, instructing the motors with relevant signals
state: Close_Bay
Once the sample is dropped, move the arm away from the rocket and trigger the bay-closing circuitry.
state: Open_Bay
Use proximity to open the payload bay, preparing it for sample retrieval.
state: PickUp
Use the gripper servo to:
Appropriately orient the gripper relative to sample.
Pick up sample & verify.
Found_Bay
!Has_Sample && Reached_Bay
state: Drop_Sample
Use the gripper servos to orient gripper relative to the payload bay and move to a minimum safe distance. Once a critical distance is reached and detected, drop and secure the sample in bay.
state: POWER_OFF
The system is in the OFF state. There is no current flowing through the circuitry and there are no moving parts.
Init_Test_Results = true
state: PAUSED
The system is in a paused, suspended state. Variables in memory retain consistent state so that the system can readily goto POWER_ON.
PowerON
PowerOFF
START
PowerOFF
RESUME
PAUSE
Has_Sample
Dropped_Sample
Refine_Metrics
Reached_Sample
Found_Sample
Refine_Metrics
Opened_Bay
Has_Sample && Reached_Bay

## Slide 2
state: POWER_OFF
The system is in the OFF state. There is no current flowing through the circuitry and there are no moving parts.
state: POWER_ON
state: Init
This is the initialization phase of the payload bay system. This state tests the payload bay electronics and safe, timely operation.
state: Closed_Bay
The Payload bay is completely closed. This state is reached when either (1) the sample is retrieved by the AGSE and secured in the bay or (2) the bay is closed after successful initialization.
state: Opened_Bay
state: Fully_Open
state: Opening
state: Closing
PowerON
Init_Tests = true
AGSE_Trigger = OPEN
Limit_Switch_1_Reached && Timeout_Expiry = false
AGSE_Trigger = CLOSE
Limit_Switch_2_Reached
Timeout_Expiry && Failure_Count < 100
PowerOFF
Timeout_Expiry && Failure_Count < 100
state: Bay_Control_Failure
This is a failure state where either (1) Initializing tests fail or (2) Repeated timeout failures during bay OPEN or CLOSE operations.
Timeout_Expiry && Failure_Count >= 100
Init_Tests = false