## Slide 1: Autonomous Ground Support Equipment Design, Construction & Implementation NASA Student Launch Initiative 2014-2015
Pranav Srinivas Kumar & William Emfinger
Vanderbilt Aerospace Club
The 2014-15 Aerospace Club was sponsored by the Department of Mechanical Engineering and the Boeing Corporation.

## Slide 2: Overview
Autonomous Ground Support
  Sample Retrieval
Design Goals
  Reliability
  Simplicity
  Robustness
Design Considerations
  Minimum degrees of freedom
  Image Processing
  Distributed Embedded System
  User Input Panel
  Model-driven software
  development

## Slide 3: Mechanical Construction (1/3)
AGSE Base Table
  25.5” tall and up to 19.5” radial reach
  Adjustable leveling feet
  Rocket stand and Base rotation system

## Slide 4: Mechanical Construction (2/3)
Lead Screw Linear Actuation
  Faulhaber 12V, 8.1W motors
  Vertical carriage supports a horizontal powertrain

## Slide 5: Mechanical Construction (3/3)
AGSE Gripper
  Optimized phalange curvature
  Acrylic “gear box”

## Slide 6: AGSE Overview

## Slide 7: AGSE Electronics (1/3)
Custom PCB
  Attaches to the BeagleBone Black as a cape
Provides power & functionality for
  Serial buffer for UART
    3.3V to 5V for servo control
  H-Bridge for Vertical Actuation Motor
  H-Bridge for Radial Actuation Motor
  Radial axis quadrature encoder
  Vertical axis quadrature encoder

## Slide 8: AGSE Electronics (2/3)

## Slide 9: AGSE Electronics (3/3)

## Slide 10: Image Processing – Sample Detection
OpenCV software library
Computer vision to classify and track observed objects in real-time
Periodic Processing
  Convert RGB image frame to HSV/Grayscale image frame
  Apply thresholding, filtering, erosion and dilation procedures
  Draw contours around detected objects
  Calculate position & relative orientation

## Slide 11: Real-time Object Tracking
Webcam
HSV Filter
Grayscale
Thresholding Filter
Bitwise-AND Result
Bounding Box

## Slide 12: Feature-based Filtering Heuristics

## Slide 13: Multiple Sample Detection

## Slide 14: Payload Bay Detection

## Slide 15: User Input Panel

## Slide 16: Software Development Robot Operating System & ROSMOD
Distributed Embedded System
Use Robot Operating System
  ROSMOD Component Model
  Modeling, Code Generation & Deployment tool suite

## Slide 17: ROSMOD Projects
Software Workspace Model
  Messages, Services & Component definitions
  Workspace & build system generation
Hardware Model
  IP Address, Architecture & network topology
Deployment Model
  Process-to-Hardware mapping
  Component Instantiation in processes
  Deployment-specific XML Generation

## Slide 18: Textual Language

## Slide 19: ROSMOD Editor – Software Model

## Slide 20: ROSMOD Editor – Hardware Model

## Slide 21: ROSMOD Editor – Deployment Model

## Slide 22: Workspace Code Generation

## Slide 23: Generated Skeleton Code

## Slide 24: Performance Assessment

## Slide 25: Performance Assessment

## Slide 26: Summary
Model-driven Component-based Engineering
Distributed Managed Embedded System
Robot Operating System & ROSMOD
Autonomous Sample Retrieval
  Periodic Image Processing
  Unknown Sample & Rocket location
  Under 5 minutes on Competition Day
We won 

## Slide 27: Vanderbilt Aerospace Club 2014-2015